# ECONA ETHERNET TESTING MANUAL

Step 1: Obtaining and Installing Netperf on Host Side

Netperf can be obtained from http://www.netperf.org/netperf/. The version we tested was netperf 2.6.0. Once you have obtained the Netperf source
code, extract it in a temporary directory then build the binaries. The following steps can be used to accomplish
this task:
1. Download Netperf to a staging area on your Linux system
2. Unzip and untar the Netperf compressed source file
#tar -xzvf netperf-x.x.x.tar.gz, where x.x.x is the current version number.
3. Change to(open) the directory where the Netperf source files were extracted (i.e., cd netperf-x.x.x, where x.x.x
is the version number)
4. Run ./configure
5. Run make
6. Run 'make install' to install the Netperf program binaries in /usr/local/bin. Note you must
be logged in as root to write to the /usr/local/bin directory
7. Enter the following command to enable the netperf's listening server.
#netserver

Step 2: Preperaing Netperf for the Target board
First 3 steps are same.
once extracted. cd to the netperf directory and issue the following command on terminal.
./configure --host=arm-linux --prefix=/home/asic/Downloads/netperf-2.6.0/netperf_target CC=/home/asic/Desktop/Econa_SDK/20100921_cns3xxx-sdk-v1.0/cns3xxx-sdk/tools/cnstools/arm-linux-le-uclibc-gcc-4.3.3-2010.05/usr/bin/arm-linux-gcc

netperf and netserver files will be created in the folder netperf_target. Copy this folder in a usb flash drive and mount it on the target board.

Step 3: Enabling the Ethernet Module of the Target Board

Please see the Reference Document title “STEPS FOR ENABLING ETHERNET MODULE OF ECONA BOARD”.

Step 4 : Enabling the USB Module and Mounting a USB Flash Drive on Target Board

Please see the Reference Document “ENABLING USB MODULE AND MOUNTING USB FLASH DRIVE ON ECONA BOARD”.

Step5 : Running Netperf

1) cd to the directory /mnt/usbdisk/netperf_target
2) enter the following command to setup a listening server on the target board as well.
#./netserver

Now both systems i.e the host and the target have the netperf's listening server installed. To run a netperf test issue the following command in the netperf_target directory

To ping a networked pc/board:

#./netperf -H 192.168.0.xxx